Message protocol and error detection

Start of a message indicated by a start char: 'A'
End of a message indicated by an end char 'B'
After the start of each message the number of received bytes are counted.

Normal operation:
A xxx xxx B A xxx xxx B
Start of a message:
- received char is 'A'
- previous char is 'B'
End of a message:
- received byte is 'B'
- received bytes = message_length

Synchronisation on startup:
Wait until:
- previous byte == 'B' (initial value upon startup of x32)
- received byte == 'A'
- if then after message_length the stop byte is received correct synchronization is assumed

Error detection:
If a message is started and after message_length the stop char is not 'B' then start counting the lost messages.
If an error is detected wait until previous byte == 'B' and received byte == 'A' and assume correct functioning again.
During the wait for correct functioning again count the number of received packets. If too much packets are received while not having correct functioning, signal an error and go into panic mode.

Connection detection:
To see whether correction is lost(no interrupts of messages received), install a timer which periodically checks what time the latest receival of a package was. Via a timestamp during the receival of a packet or by the use of a watchdog timer.